## Slide 1
Weekly Meeting
Chuck Huang
2023/12/14
Confidential, for Group internal use only
Group

## Slide 2
ASIC vs. FPGA
No SRAM1 control bit on spec. (HW designer will fix it)
BCH need software reset (CLKCON0_P0[3]) after PWR gating switch

## Slide 3
Overall Operation Loop
System initial
SD initial
READY_FOR_DATA = 1
Idle task
Security erase/erase task
Pro CSD task
Gen CMD Write task
Read task
default
bCallWriteLBA
write_data_from_hs_buf_to_flash
clr_sd_read_data_flag
FE
FTL
BE
n

## Slide 4
System Initial
100MHz = 10ns (i.e., near 90ns)
0 = Group 0 (SDCLK)
1 = Group 1 (SDCMD)
(No SRAM1 control as mentioned before)
UART, timer initial

## Slide 5
Is Ready to Sleep?
write_hs_data_to_flash_state == W_HS_DATA_TO_FLASH_IDLE
write_virtual_sd_buf_data_to_nf_state == W_VIRTUAL_SD_BUF_DATA_TO_NF_IDLE
rcv_data_state == HS_RCV_DATA_IN_IDLE
virtual_sd_data_buf_cnt == 0
sd_ready_for_nf_buf_cnt == 0
!bMulWriteTask && !bSingleWriteTask
wait_for_enter_sleep_mode
BUFFER_START_ADDR
(0x6080 @ SRAM0)
1024
16
SD_HS_CACHE_BUF_CNT
(0x5000 @ SRAM0)
512
Virtual Buffer
SD_VIRTUAL_BUF_CNT
(SLC block)
page
44

## Slide 6
Buffer Collection (Cont’d)
Buffer Name | Serve | Size | Count | Address | Location | Key Word | Note
Virtual | SD | SLC page | 44 (maximum) | SLC block | NAND | SD_VIRTUAL_BUF_CNT | Need 44 pages?
Cache | FTL | 512B | 3~9 (??) | 0x5000 | SRAM0 | SD_VIRTUAL_BUF_CNT | Performance bottleneck?
Nand Flash | BE | 1024B | 16 | 0x6800 | SRAM0 | BUFFER_START_ADDR | 

## Slide 7
Power Down Process
!WKPND && Idle
Clear wake up pending
Disable timer ISR
Enable timer ISR
Y
!WKPND && Idle &&
CMD_IDX != ERR_40
Low power enable
Disable RC
Clear wake up pending
Wake up end process
PD = 1
Y
Do not slow down clock frequency

## Slide 8
Confidential, for Group internal use only
Group
Thank you